## Slide 1: Using IDS/IPS to Identify or Prevent Industrial Network Attacks
Made possible through support from the National Science Foundation (NSF) award number 1800929

## Slide 2: Objectives
Explain the difference between an Intrusion Detection System (IDS) and an Intrusion Prevention System (IPS).
Discuss the usage cases that would make the use of an IDS more appropriate than the use of an IPS.
Describe how host and network-based IDS/IPS differ in functionality.
Describe how signature based and anomaly-based IDS/IPS differ in functionality.
Describe the difference between a false negative and a false positive.
Demonstrate how an IDS/IPS can be used to protect industrial devices such as PLCs or OPC servers.

## Slide 3: Intrusion Detection System (IDS) Basics
The purpose of an IDS is to identify potentially harmful network or system activity.
Monitor activity
Analyze activity
Alert administrator if activity is suspicious

## Slide 4: Intrusion Prevention System (IPS) Basics
The purpose of an IPS is to prevent potentially harmful network or system activity.
Monitor activity
Analyze activity
Block connection if activity is suspicious

## Slide 5: Network Based IDS/IPS
All Systems Protected
Network based IDS/IPS systems are installed at the boundary between networks and provide protection to multiple systems simultaneously
IDS/IPS at network boundary

## Slide 6: Host Based IDS/IPS
IDS/IPS installed on host
Host based IDS/IPS systems are installed on, and protect, individual hosts
Individual host protected

## Slide 7: Host based vs Network Based IDS/IPS
Can provide only generic protection
Can be highly customized for the
system being protected
Can monitor only network traffic
Can monitor both system activity and
network traffic
Protects multiple systems
Protects a single system
Installed and configured once
Installed and configured at each host
Network based
Host based

## Slide 8: Signature Based IDS/IPS
Signature based IDS/IPS systems identify suspicious activity based on predetermined patterns

## Slide 9: Anomaly Based IDS/IPS
Unusual traffic
Anomaly-based IDS/IPS systems identify suspicious activity based on it being different from normal activity
ICS System
IDS/IPS
Internet
Email to Google
Web to Yahoo
Email from Google
Web from Yahoo
FTP from Darknet

## Slide 10: Signature Based vs Anomaly Based IDS/IPS
Effective as soon as signatures are
installed
Effective only after normal traffic
baseline has been established
Requires the regular downloading and
updating of signatures
Does not need require updates
Effective against known attacks
Effective against unknown attacks
Signature based IDS/IPS
Anomaly
-
based IDS/IPS

## Slide 11: False Positives
Suspicious traffic
A false positive is said to have occurred when the system determines that normal activity is suspicious
  Can prevent normal system functionality
ICS System
IDS/IPS
Internet
Email to Google
HTTPS to Yahoo
Email from Google
HTTPS from Yahoo
FTP from Darknet
Notes: Discuss how this could potentially cause safety equipment to fail.

## Slide 12: False Negatives
Normal traffic
A false negative is said to have occurred when the system determines that suspicious activity is normal
  Can allow an attack to go undetected
ICS System
IDS/IPS
Internet
Email to Google
HTTPS to Yahoo
Email from Google
HTTPS from Yahoo
FTP from Darknet

## Slide 13: For More Information
For further information go to https://www.nl.northweststate.edu/camo or contact:
  Tony Hills – thills@northweststate.edu – 419-267-1354
  Sarah Stubblefield – sstubblefield@northweststate.edu – 419-267-1512
  Mike Kwiatkowski – mkwiatkowski@northweststate.edu – 419-267-1231
Made possible through support from the National Science Foundation (NSF) award number 1800929