## Slide 1: Secure Remote ICS Access Using a VPN and Firewall
Made possible through support from the National Science Foundation (NSF) award number 1800929

## Slide 2: Objectives
Explain basic firewall concepts.
Explain basic Virtual Private Network (VPN) concepts.
Compare different VPN technologies.
Demonstrate how the use of a firewall can prevent many remote attacks.
Demonstrate how the use of VPN secures network traffic.

## Slide 3: Firewall Basics
The purpose of a firewall is to allow authorized traffic and prevent unauthorized traffic
  Typically, outbound traffic is mostly unrestricted while inbound traffic is severely restricted

## Slide 4: Firewall Basics
Firewalls can be broadly classified into two categories
  Host based firewalls protect a single host
  Network based firewalls protect all systems on the same network segment
Host Firewall
Network Firewall

## Slide 5: VPN Basics
VPN – Virtual Private Network
  Creates a private tunnel by encrypting data prior to sending it and decrypting the data when it is received
No VPN
Unencrypted data transmitted
VPN
Data encrypted before
being transmitted

## Slide 6: VPN Basics
ziwksmsfveo
ynonfeyqvcx
Dbjxyplowgj
xmelqjtoczs
Cypher text
Encrypt
Network Tunnel
Cypher text
Encapsulatee
Secret recipe
------
12 something
2 other stuff
Plain text
Sender
Internet

## Slide 7: VPN Basics
Secret recipe
------
12 something
2 other stuff
Plain text
Decrypt
ziwksmsfveo
ynonfeyqvcx
Dbjxyplowgj
xmelqjtoczs
Cypher text
Decapsulate
Network Tunnel
Cypher text
Receiver
Internet
Hacker

## Slide 8: VPN Technologies
PPTP - Point to Point Tunneling Protocol
  Simple to setup
  Not secure
L2TP – Layer 2 Tunneling Protocol/IPSec – IP Security
  L2TP – Provides basic unsecured tunneling
  IPSec – Secures the data in the L2TP tunnel

## Slide 9: VPN Technologies
SSTP - Secure Socket Tunneling Protocol
  Uses SSL/TLS over TCP port 443 which prevents many firewall issues
OpenVPN
  Open source VPN solution which is often implemented using Linux
Other
  Many other VPN solutions exist including commonly used proprietary solutions from vendors such as Cisco